## Slide 1
PT TDK ELECTRONICS INDONESIA
TPS Business Group • BT TPS HR
Batam, Indonesia
05 April 2023
Internship Project:
Monitoring Rapid Temperature Cycle in Liquid

## Slide 2
I Made Aditya Rama P
  Internship Politeknik Elektronika Negeri Surabaya - NIM: 4120600021
  Major - Mechatronics Engineering
Sander Antonius Balisa Internship Politeknik Elektronika Negeri Surabaya - NIM: 2120600053 Major – Electronic Engineering
Project Mentor
Head of department : Mr. Mahesh Nair
Mentor : Mr. Syaifudin Muchlis
Project supervisor : Mr. Indratno Sukmandaru
Project Team

## Slide 3
Project Objectives :
The purpose of this project is to implement industrial revolution 4.0 digitalization for RTC (Rapid Temperature Cycling in Liquids) system. This project is an improvement project compared existing system.

## Slide 4
List of project benefits:
Categories | Existing System | Improvement Project
Capabilities | Up to 195 samples | Up to 3120 samples
DMM Connections | 1 DMM | Up to 16 DMM
Real-time Graph | No | Yes
Output | Text File (*.txt) | Excel File (*.xlsx) + Table Format View + Auto Graph
Bath Temperature Monitoring | No | Yes
Auto Chart Export | No (just file .txt) | Yes (Auto Create Chart and Box and Whisker)

## Slide 5
List of project benefits:
Categories | Existing System | Improvement Project
Data Storage | Text File (*.txt) | SQL Server Database
Sampling Schedule | Static | Dynamic
Output | Text File (*.txt) | Excel File (*.xlsx) + Table Format View + Auto Graph
GUI | Static | Dynamic (Customizable)
Alarm Alert | No | Yes
Email Notification | No | Yes
Hardware Settings | Non-Configurable | Configurable

## Slide 6: Machine layout
Monitoring Area

## Slide 7: Requirement
Hardware
No | Name | Brand / Type | Qty | Unit
1 | Module for thermocouple (8 thermocouple) | Advantech | 1 | Pcs
2 | Thermocouple type-K |  | 6 | Pcs
3 | Digital Multi meter Module | Keithley | 1 | Pcs
4 | Digital Multi meter |  | 1 | Pcs
4 | GPIB Cable |  | 1 | Pcs
5 | Personal Computer |  | 1 | Pcs

## Slide 8: Maximum collected samples
39 samples x 5 slots x 16 DMM = 3.120 samples
And more N computer….

## Slide 9: Hardware Components
A Digital Multi mater module used for data acquisition, switching ,data logging, for sampling data on sensor
A thermocouple module used for reading data analog on sensor and convert to digital such as temperature.
Front
Back
Front
Back

## Slide 10: Thermocouple Module for Data Collection
Hot Temperature bath
Cold Temperature bath

## Slide 11: 1. Welcome screen
Application User interface
2. Voltage Realtime Monitoring
3. Temperature Realtime Monitoring
4. Alarm Options

## Slide 12: 5. Assets Menu
Application User interface
6. Assets Thermocouple
7. Menu Equation
8. Database View

## Slide 13: 9. Export Menu
Application User interface
Export option setting type file (*.xlsx) or pdf, and setting the saving directory.
Data view before exporting

## Slide 14: 10. View data result in excel
Application User interface
View Data and auto create Chart
Data Report by Chart Box and Whisker

## Slide 15: 11. Change User Interface color setting
Application User interface
Information about samples

## Slide 16: Result Gage R&R Study - ANOVA Method
Data Analytics

## Slide 17: Installation
Hardware
View of RTC machine on front
View in RTC with Hot Temperature
View in RTC within Cold Temperature
View of RTC machine between bath
Thermocouple
Thermocouple

## Slide 18: Conclusion
Monitoring RTC (Rapid Temperature Cycling) Liquid in the
Research and Development Lab
Monitoring Temperature in real-time.
Graphical monitoring of the temperature.
Feature :
Sample Acquisition Data
Bath Temperature Monitoring
Auto create tables and graphs in excel file (*.xlsx).
Alarm System
Email Notification